## Slide 1
DEPARTMENT OF COMUPUTER, CONTROL AND MANAGMENT ENGINEERING ANTONIO RUBERTI
Students: Simone Orelli, Antonio Rapuano, Francesco Russo.
Professor: Claudia Califano
Two Wheels Self-balancing Robot
Digital Control Systems

## Slide 2
Outline
  Introduction
  Model
  Simulation
  Hardware
  Sensor Data Acquisition
  Demo
  Future Developments
  Conclusion

## Slide 3
Introduction
Goal
The aim of this project is to build a wheeled robot with the remarkable capability of autonomously maintaining balance.
Physical Structure
The heart of this project is the ambition to empower the robot with the ability to dynamically adapt to variations in its surrounding environment.
The physical structure of the robot has been designed using Autodesk Inventor and subsequently manufactured with a 3D printer.
The material chosen to print the robot is PLA, which offers good strength and rigidity.

## Slide 4
Hardware
Stepper Motor NEMA 14
Actuation Devices:
Two Wheels Self Balancing Robot 3D Model

## Slide 5
Hardware
PCB:
Voltage Regulator
Arduino Nano
Driver A4988
MPU-6050
Two Wheels Self Balancing Robot 3D Model
IDE

## Slide 6
Hardware
Two Wheels Self Balancing Robot 3D Model

## Slide 7
Hardware
Electrical Scheme
CONNECTIONS
Driver A4988:
DIR -> D2
STEP -> D3
SLEEP -> D4
RESET -> D4
MS3 -> D5
MS2 -> D6
MS1 -> D7
MPU - 6050:
SCL -> A4
SDA -> A5

## Slide 8
Model
Lagrangian Method
To find the dynamics of the TWSBR system we used the Lagrangian method, instead of the Newtonian one.
The Lagrangian function is defined as:
It is used into the Euler-Lagrange equation:
where T is the kinetic energy and V is the potential energy.
where are non-conservative (external or dissipative) generalized forces performing work on .

## Slide 9
Model
Euler-Lagrange equation
Lagrangian Method
It can be linearized about
using , and

## Slide 10
The TWSBR is an unstable system because its transfer function has an unstable pole in .
Stability
Model
Transfer Function Representation
The stepper motors make the system act like a closed loop, applying the necessary torque to reach the desired motor shaft angular speed.
Because of this, there is no need to use angular encoders, but this kind of representation requires to be tuned accurately according to the motor specifications.
Transfer function between pitch angle and motor input:

## Slide 11
Control System
Feedback signals: Angular measurements and
Control signal: Angular velocity of the stepper motor shaft
Controller
Actuators
System
Sensors
+
-
Angular Outputs
Feedback Signal
Angle Setpoint
Angle Error

## Slide 12
Control System
Actuators
System
Sensor
+
-
Feedback Signal
Angle Setpoint
Angle Error
Arduino Nano
Stepper Motor
MPU-6050
Feedback signals: Angular measurements and
Control signal: Angular velocity of the stepper motor shaft
Angular Outputs

## Slide 13
Control System
Actuators
Sensor
+
-
Feedback Signal
Angle Setpoint
Angle Error
Arduino Nano
Stepper Motor
MPU-6050
Feedback signals: Angular measurements and
Control signal: Angular velocity of the stepper motor shaft
Angular Outputs

## Slide 14
Simulation
The PID controller must take into account the delay introduced by the ZOH reconstruction filter, which can be approximated using Padé’s formula:
Continuous Controller
Continuous representation of the discrete closed loop with the PID controller:
Integral Action
Process
+
-
Output
Reference
Proportional Action
Derivative Action
+
+
+
ZOH delay

## Slide 15
Simulation
The sampling time is chosen sufficiently shorter than the maximum imposed by Shannon’s theorem considering the bandwidth of the system.
Discretized Controller
The only difference lies in the way the derivative and the integral operations are computed.
Integral Action
Process
+
-
Output
Discrete reference
Proportional Action
Derivative Action
+
+
+
Sampler
Reconstructor (ZOH)
T = 0.02 s
Kp = -50 Kd = -1 Ki = -375

## Slide 16
Simulation
Orange line: Closed-loop response when employing the continuous version of the system.
Blue Line : Closed-loop response when using the discrete implementation of the continuous controller.
Evolution of the closed-loop TWSBR system with null reference.

## Slide 17
Sensor Data Acquisition
Gyroscope:
directly measures the angular rate .
Accelerometer:
measures the gravity acceleration, which can be used to compute the angular displacement .
MPU6050
}
Sensor data fusion
+X

## Slide 18
Sensor Data Acquisition
Significant presence of measurement noise

## Slide 19
Sensor Data Acquisition
Low-pass filter + Kalman filter
Low-pass filter for high-frequency noise reduction (e.g. vibrations)
Kalman filter for sensor data fusion and state reconstruction

## Slide 20
Demo

## Slide 21
Demo

## Slide 22
Future Developments
Integrate an additional controller in cascade control configuration so that the robot can track a speed reference.
Implement an Adaptive Cruise Control (ACC) algorithm to adjust the speed to maintain a safety distance from a moving target.
Integrate an ultrasonic distance sensor (e.g. HC-SR04) to introduce the perception of its surrounding.

## Slide 23
Conclusion
The main objective of the project was to implement a control system to maintain balance for a wheeled robot.
We adopted the model-based design approach, using MATLAB and Simulink to simulate the controller's behaviour.
Our model proved to be accurate, reflecting the dynamics of the physical robot (some fine-tuning was necessary anyway).
During the implementation in Arduino, we faced significant challenges, particularly related to the limited computational capacity of the board.
However, through code optimization and streamlining, we successfully overcame these obstacles and got a working system.
The result is a robot that maintains balance in a robust fashion, demonstrated both in simulation and in the real world, proving that the model and the software are reliable, ensuring stability even in the face of external disturbance.

## Slide 24
Thanks For Your Attention